## Slide 1: Parallelized Algorithm for Persistent Feasibility in Linear Systems with Multiple, External Switching Signals
Richard Arlen Hall, Dr. Leila Bridgeman
2022 – IEEE CDC
Notes: Hello everyone. My name is Richard Hall, and I am a PhD candidate at Duke University. Today, I am presenting research carried out by my advisor, Dr. Leila Bridgeman, and me where we studied methods of ensuring persistent feasibility in large scale systems with multiple, independent switching signal found in distributed system contexts. This problem is one of the many fronts against the curse of dimensionality and advancements were made by parallelizing the problem as will be shown in the following slides.

## Slide 2: Introduction
Objective: Regulate power storage, generation, and usage in microgrid.
Challenge: Limited resources could lead to loss of power.
Example: Microgrids
Notes: We were originally motivate while studying the problem of allocating energy within the microgrid context. The internal variations in supply and load suggest a time-varying model for the system. Since a microgrid will contain limited generation and storage resources, it can be difficult to maintain consistent power under these variations.

## Slide 3: Introduction
Objective: Regulate power storage, generation, and usage in microgrid.
Challenge: Limited resources could lead to loss of power.
  Solution: Connect multiple microgrids together.
Challenge: Curse of dimensionality.
Example: Microgrids
?
Notes: One solution to this problem is to network multiple microgrids together, allowing them to share resources as needed. However, this leads to additional challenges. Namely, as microgrids are connected, centralized solutions will start to fail as the number of states grows.
CLICK
We could address this by leaving the controllers distributed and finding parallel solutions.
CLICK
Our solution to this problem is the focus of this work.

## Slide 4: Introduction
Context: Distributed, constrained, externally switched systems with non-cooperative controllers.
Objective: Compute state constraints that ensure global constraint satisfaction for all time.
Constraints: Parallelize results.
Research Objectives
?
Notes: Put a little more plainly, we are looking at distributed, constraints, externally switched systems with non-cooperative controllers. We will define these terms more precisely going forward but this hopefully provides some idea of where we are going.
CLICK
Within this context, we are looking for tightened state constraints that will allow the global system to maintain persistent feasibility.
CLICK
And finally, the solution must be parallelizable to overcome the curse of dimensionality.

## Slide 5: Externally Switched Systems
The single microgrid is an example of an Externally Switched System.
Special class of hybrid systems:
  State-based:
  Time-based:
Note: We assume disturbance is available before selecting input.
Introduction
Switch in dynamics
Switch in constraints
Switch in objectives
Notes: We turn now to a closer examination of externally switched systems in the centralized context. These are a special class of hybrid systems which are systems with discrete and continuous variables. When we say a system “switches” we mean something about it changes such as its dynamics, constraints, or objective. Here, we consider systems with a finite number of possible modes that are all known before hand.
The trigger that causes the switches can either be state or time based.
CLICK
Here, we are looking at the time based switching. Therefore, the switching signal, denoted here as the red sigma subscript is an function mapping the current time to one of a finite number of mode indices. This signal is not known before hand so switches are only sensed when they occur.
CLICK
I will note here that this work assumes the disturbance is known before selecting the input. When we introduce distributed systems, the disturbance term will account for the effects of neighboring agents so previewing the disturbance is equivalent to knowing the state of your neighbors. This slight increase in communication overhead is offset by the ability to select better inputs.

## Slide 6: Externally Switched Systems
Objective: Find states that
  Respect state constraints for current mode, and
  Can respect state constraints for any possible new mode.
Example: How fast can the car travel without violating switching speed limits?
  Naive state constraints: 0 <= v <= 25 m/s
  Safe-set state constraints: 0 <= v <= 22.5 m/s
Centralized Feasibility
Notes: As I mentioned when discussing the microgrid, our objective is to find state constraints that ensure persistent feasibility even under external switching. This goal is intuitive in the centralized case as demonstrated in the following example. Though the vehicle vehicle could legally drive any speed less than 25m/s, this may create a situation where the car cannot stop fast enough to respect a lowered speed limit. Of course, the solution is to drive slower than required to ensure we never break the speed limit. These tightened state constraints create persistent feasibility in the system.

## Slide 7: Externally Switched Systems
Objective: Find states that
  Respect state constraints for current mode, and
  Can respect state constraints for any possible new mode.
Consider constraints on the switching signals.
Centralized Feasibility
When can the
system switch?
Which modes can be switched between?
Notes: The previous example motivates some other ideas common in the literature and used in this paper. First, though we may not know when switches can occur exactly, we may be able to find some reasonable bounds. Keeping with the car, you wouldn’t expect the speed to change very rapidly or switch between two values. There is some minimum distance and, therefore, minimum dwell time between switches.
Likewise, we know from experience that speed limits won’t go from highway to neighborhood speeds in a single step. There are limitations on any speed can switch too. This illustrates constraints on which modes can between. So, in summary, we have constraints on when a switch can happen and what a mode can switch into.

## Slide 8: Externally Switched Systems
Objective: Find states that
  Respect state constraints for current mode, and
  Can respect state constraints for any possible new mode.
Consider constraints on the switching signals described as directed graphs.
Example: mode sequence from node a:
  1-1-1-3-3-2
Valid since path on graph exists!
Centralized Feasibility
Notes: These constraints can be packed cleanly into directed graph constraints. These graphs have nodes that the switching signal moves between. The label on the node indicates which mode the system is in and the connections describe how the signal can evolve over the graph. For example, the switching signal could start at node a, then go to node b and sit for two steps, then go to node e, f, and c respectively. This would cause the system to be in mode 1 for 3 steps, mode 3 for 2 steps, and end in mode 2.

## Slide 9: Externally Switched Systems
Assign state constraints to each node.
Let inputs exist for every that will move the state into one of the successor sets depending on how the switching signal evolves.
Centralized Feasibility
Notes: Finally, after this discussion, we are ready to establish persistent feasibility in the centralized system. We do this by assigning a state constraints, called a safe-set, to every node in the switching signal’s constraint graph. Each of these sets must be subsets of the corresponding state constraints in the same way our new speed limit had to be less than or equal to the posted speed limit.
CLICK
Furthermore, no matter how the switching signal evolves, the states in these safe-sets must be able to enter the new safe-set in a single time step. If you think about the switching signal moving over the graph for all time, this condition ensure that the sequence of corresponding safe-sets can be traversed by the state using feasible inputs. Since these safe-sets are subsets of the state constraints, we ensure that the system never violates it’s state constraints.
CLICK
All the safe-sets over the graph make up a safe-set collection. Its formal definition is shown here and the additional notation is defined in the paper.

## Slide 10: Externally Switched Systems
Centralized Feasibility
Notes: The procedure for finding the safe-set collection for a centralized system is described here. While this algorithm uses notation introduced in this paper, it is a directly adapted from previous works such as Computation of Maximal Safe Sets for Switching System by Santis and others in 2004. The only substantive difference is in the use of pre-sets operations that use disturbance-previews.
CLICK
These lines make up the core of the algorithm. The outer for loop iterates through each node in the constraints graph while the inner for loop iterates through each out-neighbor of the current node. By intersecting the current guess for the node’s safe-set with the pre-set of the neighbor’s current safe-set, the algorithm converges to the maximal safe-set collection.
CLICK
This was proven in Lemma 1 in the paper.

## Slide 11: Externally Switched Systems
Challenge: The central solution
  Does not scale well
  Only has one switching signal
Parallelized Feasibility
Notes: Up till know, we have only been looking at the centralized case. While this has provided intuition and the results will be used later, remember that we are interested in the case where the system is made up by several distributed agents, each with their own switching signal. While the centralized techniques could be used by merging the switching signal constraints into a single graph with one switching signal amalgamating all the independent switching signals, this would quickly become untenable as will be shown in the numerical example. Without the centralized option, we turn to developing the parallelized approuh. Specifically, we are looking at systems with the dynamics shown here. These are the dynamics for agent 1 which is where the 1 superscripts come from. The last term defines the effect each neighbor’s state has on the agent. Like I said previously, these states are assumed to be known so, therefore, this term represents a known, time-varying affine term.
CLICK
To clean the notation, we replace this term with a bounded disturbance term.
CLICK
Resulting in this system. This is exactly like the centralized case with one key difference: The size of the disturbance set is dependent on the neighbors safe-sets. This means we can’t find our safe-sets until we find those of our neighbors. Likewise, however, we can’t find our neighbor’s safe-set collection until we know our own. To escape this circular dependency, we designed the key parallelizable algorithm.

## Slide 12: Solution Overview
Algorithm Design – Parallelized Algorithm
Start with trivial feasible regions (equilibrium points).
Notes: We show both the formal algorithm and a graphical representation of it here. This algorithm finds safe-set collections for every agent in a networked system where each agent has its own external switching signal. Each iteration repeats the same steps twice. The first time results in invalid safe-set collections for each agent while the second time produces valid safe-set collections. Specifically, the algorithm starts with every agent having trivial safe-set collections equal to the origin. For the linear system described, these will always satisfy the safe-set requirement but will obviously be too restrictive. Critically, however, the first iteration starts with valid safe-set collections. Then …
CLICK
…each iteration begins with every agents finding the convex hull of its safe-set collection and sharing it with the other agents. This is then used to find the disturbance bounds for each agent. For the fist iteration, this will be the origin but it will be non-trivial during later iterations.

## Slide 13: Solution Overview
Algorithm Design – Parallelized Algorithm
Start with trivial feasible regions (equilibrium points).
Compute safe-sets under disturbance bounds.
Notes: Next, the centralized algorithm is used to find new safe-set collections for each agent under the newly computed disturbance bounds. Again, the first iteration has 0 disturbance bounds so the safe-sets will not consider neighboring disturbances. The safe-set collection in each agent will grow larger but will be infeasible under the new, non-trivial disturbances now that the agents have non-trivial safe-set collections.

## Slide 14: Solution Overview
Algorithm Design – Parallelized Algorithm
Start with trivial feasible regions (equilibrium points).
Compute safe-sets under disturbance bounds.
Share convex hull of new, larger safe-sets.
Notes: To rectify this, the process is repeated. The newly computed safe-set collections which are to large are used to find disturbance bounds. It is proven in the paper that these new disturbance bounds will always be larger than the first time through this iteration. These larger disturbance bounds are then…

## Slide 15: Solution Overview
Algorithm Design – Parallelized Algorithm
Start with trivial feasible regions (equilibrium points).
Compute safe-sets while assuming neighbors are using equilibrium points.
Share convex hull of new, larger safe-sets.
Recompute safe-sets with larger guesses for neighbors.
Notes: Passed to each agent and they recompute their local safe-set collections. These will be smaller than the first time through due to the larger disturbance bounds. This means that the disturbance bounds realized by these smaller safe-set collections are smaller than what they were designed to handle. Therefore, they are still feasible even though their disturbance bounds where wrong. In summary, we start each iteration with local guesses of safe-set collections that are smaller than optimal but valid. Lines 6-10 make these collects larger but invalid. Finally, lines 11-15 returns us to smaller safe-set collections that are valid and larger than the initial sets.

## Slide 16: Solution Overview
Algorithm Design – Parallelized Algorithm
Lemma 2: Every iteration of Algorithm 2 produces a valid safe-set collection for every agent in the system (informal).
Notes: These results are summarized and proved in Lemma 2 in the paper. It is stated here informally without the extra notation.

## Slide 17: Numerical Example
Coupled spring-mass-damper system with switching masses.
Description
Notes: This algorithm was run on a system representing a grid of spring-mass-damper systems where each mass switches between three discrete values. Each agent is constrained to move in a single dimension so they only have 2 states each. Each agent has their own switching signal with the graph based constraints shown here. So the system has 9 agents, each with 2 states and 1 switching signal with 15 modes and, therefore, 15 safe-sets.

## Slide 18: Numerical Example
Storage analysis
Complexity
Approach | # Safe-Sets | Vertex/Safe-Set | Dim/Vertex | Bits/Dim | Storage Required
Centralized |  |  |  |  | 52.59 TB
Parallelized |  |  |  |  | 3.24 KB
Approach | # Safe-Sets | Vertex/Safe-Set | Dim/Vertex | Bits/Dim | Storage Required
Centralized |  |  |  |  | 52.59 TB
Parallelized |  |  |  |  | 3.24 KB
Notes: Before I get to the results, I want to point out the benefits of this work and why the centralized solution fails. If we were to combine the switching signals of the 9 agents into a single agent with one graph, that graph would need 15^9 nodes. Since each node needs its own safe-set, simply the storage would be 52.59TB for the simplest case where each safe-set has n+1 vertices. Compare this with the 3.24 KB required for the work presented here. Hopefully, it is obvious why you won’t be seeing any comparison to the centralized case!

## Slide 19: Numerical Example
Computed using consumer PC
Results
Notes: These plot demonstrate the grow-contract cycle of each iteration and the convergence of the safe-set for one node in one agent. The other 135 safe-sets had similar convergence results. Notice in the scatter plot, that the x-axis represents the iteration number and the y-axis is a log plot showing how the safe-set collections changed in size. Black indicated they grew while red indicates they shrunk. We notice that, as expected, the safe-sets first grew and then shrunk each iteration until they converged. On the last iteration, the systems converge so there is no change. Since this is a log plot, these 0 values could not be shown which is why there is an odd number of steps shown.

## Slide 20: Conclusion
Context: Distributed, constrained, externally switched systems with non-cooperative controllers.
Objective: Compute state constraints that ensure global constraint satisfaction for all time.
Constraints: Parallelize results.
Notes: The numerical example and accompanying lemmas establish this work’s effectiveness at meeting the stated objectives of the project. Using this, persistent feasibility in networked, externally switched systems can be established in a numerical tractable manner.

## Slide 21: Questions?
Email: Richard.A.Hall@duke.edu
Acknowledgements
Partially funded by ONR-YIP
Code: N00014-23-1-2043
Notes: Thank you for your attention, Any questions can be emailed to me at the following address.