## Slide 1: Parallelized Algorithm for Persistent Feasibility in Linear Systems with Multiple, External Switching Signals
Richard Arlen Hall, Dr. Leila Bridgeman
2022 – IEEE CDC

## Slide 2: Introduction
Objective: Regulate power storage, generation, and usage in microgrid.
Challenge: Limited resources could lead to loss of power.
Example: Microgrids

## Slide 3: Introduction
Objective: Regulate power storage, generation, and usage in microgrid.
Challenge: Limited resources could lead to loss of power.
  Solution: Connect multiple microgrids together.
Challenge: Curse of dimensionality.
Example: Microgrids
?

## Slide 4: Introduction
The single microgrid is an example of an Externally Switched System.
Special class of hybrid systems:
  State-based:
  Time-based:
Externally Switched Systems
Switch in dynamics
Switch in constraints
Switch in objectives

## Slide 5: Introduction
Objective: Find states that
  Respect state constraints for current mode, and
  Can respect state constraints for any possible new mode.
Consider constraints on the switching signals.
Externally Switched Systems
When can the
system switch?
Which modes can be switched between?

## Slide 6: Introduction
Objective: Find states that
  Respect state constraints for current mode, and
  Can respect state constraints for any possible new mode.
Example: How fast can the car travel without violating switching speed limits?
  Naive state constraints: 0 <= v <= 25 m/s
  Safe-set state constraints: 0 <= v <= 22.5 m/s
Externally Switched Systems

## Slide 7: Introduction
Externally Switched Systems
Objective: Find states that
  Respect state constraints for current mode, and
  Can respect state constraints for any possible new mode.

## Slide 8: Introduction
Objective: Find states that
  Respect state constraints for current mode, and
  Can respect state constraints for any possible new mode.
Consider constraints on the switching signals described as directed graphs.
Example: mode sequence from node a:
  1-1-1-3-3-2
Valid since path on graph exists!
Externally Switched Systems - Feasibility

## Slide 9: Introduction
Assign state constraints to each node.
Let inputs exist for every that will move the state into one of the successor sets depending on how the switching signal evolves.
Externally Switched Systems - Feasibility

## Slide 10: Introduction
Algorithm
Externally Switched Systems - Feasibility

## Slide 11: Introduction
Useful for making intractable problems tractable.
Two approaches:
  Cooperative – work together for a global objective.
  Non-cooperative – Work separately for local objectives.
Assumes a preview of disturbance, decreasing conservatism.
Distributed Systems
Add equations and Figure

## Slide 12: Solution Overview
Algorithm Design – Parallelized Algorithm
Start with trivial feasible regions (equilibrium points).

## Slide 13: Solution Overview
Algorithm Design – Parallelized Algorithm
Start with trivial feasible regions (equilibrium points).
Compute safe-sets while assuming neighbors are using equilibrium points.

## Slide 14: Solution Overview
Algorithm Design – Parallelized Algorithm
Start with trivial feasible regions (equilibrium points).
Compute safe-sets while assuming neighbors are using equilibrium points.
Share convex hull of new, larger safe-sets.

## Slide 15: Solution Overview
Algorithm Design – Parallelized Algorithm
Start with trivial feasible regions (equilibrium points).
Compute safe-sets while assuming neighbors are using equilibrium points.
Share convex hull of new, larger safe-sets.
Recompute safe-sets with larger guesses for neighbors.

## Slide 16: Solution Overview
Provide supporting properties and lemmas
Algorithm Design – Parallelized Algorithm

## Slide 17: Numerical Example
Coupled spring-mass-damper system with switching masses.
Description

## Slide 18: Numerical Example
Centralized approach
  Actual size would be orders of magnitude larger.
Complexity
Approach | # Safe-Sets | Vertex/Safe-Set | Dim/Vertex | Bits/Dim

## Slide 19: Numerical Example
Computed using consumer PC
Results

## Slide 20: Conclusion
Summary of results
Future work

## Slide 21: Questions?
Email: Richard.A.Hall@duke.edu