## Slide 1: Parallelized Algorithm for Persistent Feasibility in Linear Systems with Multiple, External Switching Signals
Richard Arlen Hall, Dr. Leila Bridgeman
2022 – IEEE CDC

## Slide 2: Introduction
Consider a simple microgrid.
Limited resources could lead to loss of power.
Illustrative Example

## Slide 3: Introduction
Consider a simple microgrid.
Limited resources could lead to loss of power.
We could connect multiple systems.
Illustrative Example
?

## Slide 4: Introduction
The single microgrid was an example of an Externally Switched System.
Special class of hybrid systems:
  State-based:
  Time-based:
Externally Switched Systems
Switch in dynamics
Switch in constraints
Switch in objectives

## Slide 5: Introduction
Goal: Find states that
  Respect state constraints for current mode, and
  Can respect state constraints for any possible new mode.
Problem is helped by constraints on the switching signals.
Externally Switched Systems - Feasibility
When can the
system switch?
Which modes can be switched between?

## Slide 6: Introduction
Goal: Find states that
  Respect state constraints for current mode, and
  Can respect state constraints for any possible new mode.
Example: A car under a 25 m/s speed limit can detect speed limit changes 45m beforehand. The speed limit can only change by 10 m/s at a time and the car can decelerate at 3.125 m/s^2. How fast can the car be going so that it will never violate new speed limits?
  Naive state constraints: 0 <= v <= 25
  Safe-set state constraints: 0 <= v <= 22.5
Externally Switched Systems - Feasibility
Add figure

## Slide 7: Introduction
Goal: Find states that
  Respect state constraints for current mode, and
  Can respect state constraints for any possible new mode.
Problem is helped by constraints on the switching signals described as directed graphs.
Example mode sequence from node a:
  1-1-1-3-3-2
Valid sequence since path on graph exists
Externally Switched Systems - Feasibility

## Slide 8: Introduction
Assign state constraints to each node.
Let inputs exist for every that will move the state into one of the successor sets depending on how the switching signal evolves.
Externally Switched Systems - Feasibility

## Slide 9: Introduction
Algorithm
Externally Switched Systems - Feasibility

## Slide 10: Introduction
Useful for making intractable problems tractable.
Two approaches:
  Cooperative – work together for a global objective.
  Non-cooperative – Work separately for local objectives.
Assumes a preview of disturbance, decreasing conservatism.
Distributed Systems
Add equations and Figure

## Slide 11: Solution Overview
Algorithm Design – Parallelized Algorithm
Start with trivial feasible regions (equilibrium points).

## Slide 12: Solution Overview
Algorithm Design – Parallelized Algorithm
Start with trivial feasible regions (equilibrium points).
Compute safe-sets while assuming neighbors are using equilibrium points.

## Slide 13: Solution Overview
Algorithm Design – Parallelized Algorithm
Start with trivial feasible regions (equilibrium points).
Compute safe-sets while assuming neighbors are using equilibrium points.
Share convex hull of new, larger safe-sets.

## Slide 14: Solution Overview
Algorithm Design – Parallelized Algorithm
Start with trivial feasible regions (equilibrium points).
Compute safe-sets while assuming neighbors are using equilibrium points.
Share convex hull of new, larger safe-sets.
Recompute safe-sets with larger guesses for neighbors.

## Slide 15: Solution Overview
Provide supporting properties and lemmas
Algorithm Design – Parallelized Algorithm

## Slide 16: Numerical Example
Coupled spring-mass-damper system with switching masses.
Description

## Slide 17: Numerical Example
Centralized approach
  Actual size would be orders of magnitude larger.
Complexity

## Slide 18: Numerical Example
Display sets and runtime.
Maybe create plots of set areas converging.
Results

## Slide 19: Conclusion
Summary of results
Future work

## Slide 20: Questions?
Email: Richard.A.Hall@duke.edu